8051 Assembler Directives

- Instructions to the Assembler

  - Not translated into machine language

  - Not executed by the CPU

- Directives pass information to the assembler

  - e.g. Where to start the program (ORG)

- Assembler Directive Format
	Name		Directive	Argument	Comments
	TRATE	EQU		10		;Tax rate

# Name

  - Similar to a label in an instruction

# Not in all directives

  - Must begin with a letter and end with a space

- Directive

# Mnemonic for the directive

# Similar to the op-code in an instruction

  - Must begin with a letter and end with a space or carriage return (CR)

- Argument

  - Memory address or numeric value used with the directive

  - Must begin with a space and end with a semicolon (;) or carriage return (CR)

- Comment

  - Like the comment in an instruction

  - Must begin with a semicolon (;) and end with a carriage return (CR)

# Commonly Used Directives
       EQU			ORG 			
       DB			
       DW 			END

- ORG

  - ORiGinate

  - Sets the instruction pointer to the starting address of the program

- DB

  - Define Byte

  - Allocates, defines and names a byte space in memory

    - e.g.   DATA1		DB		9FH

      - DATA1 will be associated with the memory location containing 9F

- DW

  - Define Word

  - Same as DB but allocates two consecutive memory locations

- EQU

  - EQUate

  - Associates a name with a value

- END

  - Tells the assembler there are no more instructions to assemble